## Slide 1
Electrochemically Mediated Photoredox Catalysis
Matthew Albritton
Group Meeting
January 23, 2024
e-

## Slide 2
Outline
Photoredox Catalysis vs. Synthetic Electrochemistry
Electrochemically Mediated Photoredox Catalysis (e-PRC)
Photoexcited Electrochemically Generated Radical Ion Photocatalysts
Electrochemically Regenerated Photocatalysts
Relative Advantages/Disadvantages
Prototypical Modern Examples

## Slide 3
Photoredox Catalysis & Synthetic Electrochemistry:
Redox Initiation
Synthetic Electrochemistry

## Slide 4
Photoredox Catalysis & Synthetic Electrochemistry:
Redox Initiation
Photoredox Catalysis

## Slide 5
Photoredox Catalysis: Advantages
Redox potential of excited photocatalyst is independent of energy input
Redox-neutral reactions are very efficient as PC can act as both reductant and oxidant
Homogenous reaction conditions

## Slide 6
Photoredox Catalysis: Disadvantages
Net oxidative or reductive reactions usually* require stoichiometric redox agents
Redox window limited by energy of visible light photons, up to 2.8 V
Other reaction components may experience photodegradation
Some PCs are very expensive
Tuning redox window can require synthesizing new catalysts

## Slide 7
Synthetic Electrochemistry: Advantages
Divided Cell
Undivided Cell
Divided cell allows for isolation of working electrode redox activity
e-
e-
Pt
M =
Zn, Mg, Cu, etc.
Potentiometers allow for easy variation of redox potential
High, localized concentration of radicals can enable radical coupling reactions and 2-electron redox reactions
Stoichiometric soluble redox agents not required. Pt cathode can reduce H+, sacrificial anodes can supply electrons

## Slide 8
Synthetic Electrochemistry: Disadvantages
Spatial separation of anodic and cathodic reactions makes redox-neutral reactions more difficult
e-
Organic solvents have a high resistivity, overpotentials are typically required to obtain acceptable reaction rate especially as reactant concentration decreases. This leads to undesired side reactions.
These same reactions can be undesired side reactions
>1 mm

## Slide 9
Side by Side Comparison

## Slide 10
Side by Side Comparison
Verschueren, R.H.; De Borggraeve, W.M. Molecules 2019, 24, 2122
Zhang, S.; Li, L.; Xue, M.; Zhang, R.; Xu, K.; Zeng, C. Org. Lett. 2018, 20, 3443–3446.
Moon, Y.; Jang, E.; Choi, S.; Hong, S. Org. Lett. 2018, 20, 240–243.

## Slide 11
Limited Redox Window
Many desirable substrates possess reduction potentials or C-H BDEs too high for photoredox catalysis or electrochemistry to enable functionalization.

## Slide 12
Electrochemically Mediated Photoredox Catalysis
Photoexcited Electrochemically Generated Radical Ion Photocatalysts
Electrochemically Regenerated Photocatalysts

## Slide 13
Electrochemically Mediated Photoredox Catalysis
Electrochemically Regenerated Photocatalysts

## Slide 14
Electrochemically Mediated Photoredox Catalysis
Electrochemically Regenerated Photocatalysts
66-90% yield
Oxidant-sensitive

## Slide 15
Electrochemically Mediated Photoredox Catalysis
Photoexcited Electrochemically Generated Radical Ion Photocatalysis
Standard
Photocatalysis
Electrochemically Regenerated Photocatalysis

## Slide 16
Electrochemically Mediated Photoredox Catalysis
Photoexcited Electrochemically Generated Radical Ion Photocatalysis

## Slide 17
Electrochemically Mediated Photoredox Catalysis
Photoredox Catalyzed Method:
Restricted to electron-rich arenes due to limited redox window

## Slide 18
e-PRC Oxidative Functionalizations

## Slide 19
e-PRC Oxidative Functionalizations

## Slide 20
e-PRC Reductive Functionalizations

## Slide 21
e-PRC Reductive Functionalizations
Reductive Aryl Halide Substitution Mechanism

## Slide 22
Summary
Photoelectrochemistry can enable reactions possessing the best qualities of both photoredox catalysis and electrochemistry while also enabling new reactivity
Replace stoichiometric redox agents in photoredox chemistry
Enable transient super-oxidants and super-reductants
Future prediction: Electrometallophotochemistry?

## Slide 23
Questions?